## Slide 1: AOI AI
Jan 2023

## Slide 2: Background / Objectives:
Background / Problem:
The AOI false-call with manual judgment operation which bring us inconsistent test result and low productivity(current AOI H/C 28).
Objective:
AOI process improvement though AI solution to reduce the 12 DL H/C (Target: BU6- 3 lines AOI DL H/C & Cisco- 3 lines DL H/C; total of 12 DL H/C for 2 shifts).
Process Affected:
AI judges the result of the False Call of the AOI machine and stores the result in the database. The client clicks Good or NG on the interface to obtain the result from the database.
Stake Holder: ME

## Slide 3: Team Members
No | Name | Job Title | Functional Department | Email
1 | CL Yeoh | Site Test Engineering & Innovation Leader | TE | cl.yeoh@flex.com
2 | Sam Wong | Site ME leader | ME | Sam.Wong@flex.com
3 | Seng Heng Eeow | Technical Ops Leader | TE | sh.eeow@flex.com
4 | Dean Zheng | Sr. Equipment Engineer | ME | dean.zheng@flex.com
5 | Rachel Li | Sr. Software Development Engineer | TE | rachel.li2@flex.com
6 |  |  |  | 
7 |  |  |  | 
8 |  |  |  | 

## Slide 4
AOI management procedure
Client
False - Call
AOI Machine
AOI Software Interface
Trained Operator
Check and click NG / Good
Manual control
Well-experienced Operator

## Slide 5
AOI AI management procedure
Passer Download IMG
Client
Pass the AI Result From DB
False - Call
AOI Machine
AI Judge IMG Result and Save in DB
Passer
AI Program
DB
Client Program
AOI Software Interface
Auto click NG / Good Base on AI Result in the interface
No Operator Control
Duplicate on different lines
KY Total time delay 16 s
ViTrox 0 s
KY Time Delay :10 s
ViTrox : 0 s
Time Delay : 0 s
Time Delay : 6 s

## Slide 6
Topological Diagram

## Slide 7: Machine Learning Training Process
Data Collect
Data preprocessing
Feature Extraction
Model Selection and Training
Model Evaluation
Optimize and Deploy

## Slide 8
Model Training Details
Data Collect
Data Analysis
Data cleaning
Sampling
Feature Extraction
Missing value calculation
Quantify Feature Binarization
Qualitative Feature Encoder
Data Conversion
Feature Selection
Dimension Reduction
Training
Predict
Assessment
Dimensionless
End
Start
Model Training

## Slide 9: BP Details
Base on the location and material type and image appearance to be separated 93 kinds classification as below,including the false call and true fail.
Brain Training Code Explanation
Classification
Resnet50 Model and Train
Code
Training Result : Brain
define model
Read Images and encode with LabelEncoder
import features and labels, then split them in training and testing with defined split ratio, the test_size
train and evaluate with LogisticRegression model, then plot confusion matrix
collecting discriminative,generate features and labels

## Slide 10: BP Details
The passer monitor the AOI database every 10 seconds. It would download the Image to local folder from the
DB once it check the AOI Machine Fales Call the image.
Passer
Image Folder

## Slide 11: BP Details
The AI program real time monitoring the image folder, if it download new image successfully,
Then the AI program would judge this image is NG or Good Result and Save the Result in local database.
AI Progress
Local Database
Image Folder

## Slide 12: BP Details
The Client program monitor the log, it would get the database’s AI result through the log’s PCBGUID.
The program would auto click NG / Good button on the AOI Software Interface once it get the AI’s result.
Client Program
Log’s GUID Match DB’s GUID

## Slide 13: BP Details
Wb site to monitor the AI Accuracy and Test Escape report. And also apply for the location image details info.

## Slide 14: Implement KY AOI Automation Detail
New Record in Log File
AOI False Call
Client Program Read Log info and Get AI Result in Local DB
Client Program Auto Click NG/Good
Software Clear the Image
Maintain
AOI False Call
New Record In AOI DB
Server
Next
Next
Passer Collect Data and Image from AOI DB
AI Brain Judge the Image Result and Save Local DB

## Slide 15: Implement ViTrox AOI Automation Detail
Generate Post File
New Index File in Folder
AOI False Call
Client Program Get Local DB’ AI result
New Blank Defect Folder
Client Program Auto Click NG/Good
Software Clear the Image
Maintain
AOI False Call
New Data and Image in Folder
Server
Next
Next
Passer Collect Data and Image from Folder
AI Brain Judge the Image Result and Save Local DB

## Slide 16: Line AI Accuracy
C19D
Total 1095 Qty
AI Correct 1054
AI Accuracy 96.26%
Test Escape 21
C23A
Total 233 Qty
AI Correct 208
AI Accuracy 89.27%
Test Escape 12
C20C
Total 835 Qty
AI Correct 809
AI Accuracy 96.89%
Test Escape 10
C23C
Total 103 Qty
AI Correct 95
AI Accuracy 92.23%
Test Escape 5
C23B
Total 2087 Qty
AI Correct 2013
AI Accuracy 96.45%
Test Escape 48
C19C
Total 9607 Qty
AI Correct 9117
AI Accuracy 94.9%
Test Escape 317
The data monitor from 2022-09-17 19:24:40 to 2022-12-12 19:24:40.

## Slide 17
Operations/ Station | Problem | Action Taken | Results |  |  |  |  |  | 
PCBA/SMT | AOI Machine fail the location within the PCB image, the well-experience operator manual open the image and then click the NG / Good result on the software interface one by one. | AOI Machine fails the location image, AI auto check the fail image and judge this image is NG / Good. The Client program auto click the NG / Good button on the AOI Software instead of manual operation. 6 lines is already install the AOI AI program. Total 12 head cut need improve including day shift and night shift. Hard saving : 870*12=10440 | CTQ (UoM/Criteria) | Before | After | % Improved | Savings |  | 
 |  |  |  |  |  |  | Hard (USD/ month) | Soft (USD/ month) | Inventory /AR/AP (USD)
 |  |  | AOI AI lead time (Online) reduction (Hr/Model) | 3.65*12 / Hr | 0 | 100 | 10440 |  | 
Customer |  |  |  |  |  |  |  |  | 
All |  |  |  |  |  |  |  |  | 
Method of Sustaining |  |  |  |  |  |  |  |  | 
Title : AOI AI
Before Kaizen
After Kaizen

## Slide 18
Introduced AOI AI auto judge the fail image online to replace manual operation, and do the head cut result as target.
BEFORE
AFTER
RESULT
AOIAI Immersion Technology Application in Factory
Engineer online training new operator face to face to learn kinds of AOI fail situation.
AOI Machine fail the PCB image and hold on the software interface.
Operator open the image location content one by one confirm and click the NG / Good result.
Collect and training AI brain by kinds of AOI Image defect Code.
AOI Machine fail the PCB image and hold on the software interface.
2
2
Passer download the AOI fail image and AI auto judge the location image as NG / Good Result and save in database.
1
1
3
Client program monitor the log and auto get the database’s location AI result then auto click the NG / Good button on the software interface.
4
3
Headcount
12 People
0 People

## Slide 19
Best Practice Implementation Method and Procedure
Tools developed and deploy:
Python – AI Brain Training and judge result
VS – Passer and tool for interface development
AI Framework – TensorFlow
Training Mode – Self-supervised Learning
Model - ResNet50
Algorithm - Logistic Regression

## Slide 20: Contact for Yokoten
No | Name | Job Title | Functional Department | Email
1 | Rachel Li | Sr. Software Development Engineer | TE | rachel.li2@flex.com
2 | Dean Zheng | Sr. Equipment Engineer | ME | dean.zheng@flex.com

## Slide 21: Q&A
Is the capability of AI algorithm and machine learning the site's own, or is it cooperated with a third party?
It is to directly call third-party open source algorithms and models
Is there an official flex AI software tools to use? Any comparison vs. Flex criteria and benefit, please add 1page comparison
No, this system was developed by B11 Site.
if you use AI to train, can you save the data?
We use our own servers to save image and training, so the data is safe.
Is your AI calculation cater to latest technology? May cross sharing with Suhong - Si Hong team
The automated training step is need refined to improve accuracy; Also,the details have also been shared with them.

## Slide 22: Thank You